## Slide 1: Methane retrievals from Sentinel-5 Precursor, PRISMA, EnMAP and EMIT and corresponding emission estimates of localized sources
Michael Buchwitz, Oliver Schneising-Weigel, Stefan Noël, Maximilian Reuter, Michael Hilker, Jonas Hachmeister, Heinrich Bovensmann, John P. Burrows and Hartmut Boesch
University of Bremen, Institute of Environmental Physics, Germany
Frances Reuland, Adam Brandt
Department of Energy Science and Engineering Doerr School of Sustainability, Stanford University, CA, USA
Taylor Adams, Eric A. Kort
Department of Climate and Space Sciences and Engineering, University of Michigan, Ann Arbor, MI, USA
v2, 23-June-2025
Methane controlled releases 2024/2025:

## Slide 2: IUP-UB: Funding through various projects
Methane
Emissions
Detection
Using
Satellites
Assessment (MEDUSA)

## Slide 3: Satellite XCO2 and XCH4 retrievals …
CCI Integration Meeting, ECMWF, 14-16 March 2011
SCIAMACHY
GOSAT
OCO-2
GOSAT-2
SCIAMACHY
+ TROPOMI/S5P, PRISMA, EnMAP, EMIT, …
+ future S5, GOSAT-GW, CO2M, …
GOSAT
GOSAT-2
See also: https://climate.copernicus.eu/esotc/2024/trends-climate-indicators

## Slide 4: Satellite XCH4 retrievals …
CCI Integration Meeting, ECMWF, 14-16 March 2011
SCIAMACHY
GOSAT
GOSAT-2
Methane growth rate in 2024
high (~ 8 ppb) but not record high
See also: https://climate.copernicus.eu/esotc/2024/trends-climate-indicators
+ TROPOMI/S5P, PRISMA, EnMAP, EMIT, …
+ future S5, GOSAT-GW, CO2M, …

## Slide 5: Satellite XCO2 retrievals …
CCI Integration Meeting, ECMWF, 14-16 March 2011
SCIAMACHY
GOSAT
OCO-2
GOSAT-2
XCO2 growth rate very high in 2024: ~ 3 ppm !
See also: https://climate.copernicus.eu/esotc/2024/trends-climate-indicators

## Slide 6: XCO2 and surface CO2 growth rates …
CCI Integration Meeting, ECMWF, 14-16 March 2011
3.75 ppm (global)
3.33 ppm (Mauna Loa)
CO2 surface data:
XCO2 growth rate very high in 2024: ~ 3 ppm !
See also: https://climate.copernicus.eu/esotc/2024/trends-climate-indicators

## Slide 7: Emission estim. algos for localized sources
https://doi.org/10.6028/NIST.IR.8575
Q[t/h] = ΔΩ[t/km2] * Δy[km] * U[km/h]
Emission ~ Column enhancement * Wind speed
ΔΩ
Δy
U
Integration of column enhancements times wind speed along transects perpendicular to wind / plume direction

## Slide 8: TROPOMI/S5P XCH4 & methane emissions
Schneising et al., ACP, 2020
Schneising et al., AMT, 2023
Emission estimates via Cross-Sectional-Flux (CSF) method
for 2018-2019
Emissions & relative leakage from oil & gas fields
Available from:
https://www.iup.uni-bremen.de/carbon_ghg/products/tropomi_wfmd/
https://climate.esa.int/en/projects/ghgs/
https://catalogue.ceda.ac.uk/
wind

## Slide 9: Potential persistent emission hotspots
www.esa.int
Permian
Oil and gas
Automated persistent hotspot detection, quantification, and source type assignment based on monthly data
South Sudan
Wetland
Turkmenistan
Oil and gas
USCB
Coal
Madrid
Landfills
Queensland
Coal
Vanselow et al., ACP, 2024
Emission estimates based on TROPOMI/S5P WFMD v1.8 XCH4 retrievals & mass balance method:
217 Potential Persistent Source Regions (PPSRs) detected (2018 - 2021)

## Slide 10: TROPOMI/S5P XCH4 WFMD v2.0
TROPOMI/WFMD v2.0
Better resource efficiency due to reduced memory consumption of machine learning quality filter
Improved accuracy and precision according to validation with TCCON
More rigorous filtering of specific aerosol events over bright surfaces
Otherwise, higher data yield, especially for mid and high latitudes
New
v2.0
v1.8
v2.0
v1.8
v2.0
Filesize:
Random Forest
XGBoost
Available from: https://www.iup.uni-bremen.de/carbon_ghg/products/tropomi_wfmd/
Bodélé Depression (Chad)
Challenging retrieval conditions (surface + dust storms)

## Slide 11: Emissions: Cross-Sectional-Flux (CSF) algo
(*)
(*) Current baseline: Matched Filter (MF)
Level 1 (L1)
Level 2 (L2)
Level 4 (L4)
L2e -> L4
L2 -> L2e
L1 -> L2
Details see poster
Noël et al., Development of a Level 1 to Level 4 processing system for estimating greenhouse gas emissions of localized sources: Methane emissions as derived from Sentinel-5 Precursor, PRISMA, EnMAP
Today in area X5 zone N 17:45-19:00

## Slide 12: Methane emission estimates: CSF method
TROPOMI/S5P (CSF v1.6)
EnMAP (HiFi-MF & CSF v1.6)
Box size (default): 100 x 100 km2
Wind: PBL average (ERA5)
Box size (default): 0.5 x 0.5 km2
Wind: 10 m (ERA5)
Input: Level 2: XCH4 WFMD v1.8
Input: Level 1
Released: 1.1 t/h
(Sherwin et al., 2022)
73 +/- 24 t/h (Qual=OK)
1.5 +/- 0.6 t/h (Qual=OK)
3 hours after overpass
Quality flag: Qual=OK (QF=0) means:
Enough data in box (e.g., > 90% of area covered)
Wind not too low (wind speed > 1 m/s)
Uncertainty (1-sigma): Several terms added quadratically: (i) Stddev of emissions per cross-section,
(ii) wind (variability + 0.5 m/s), (iii) other (20%)

## Slide 13: Methane: S5P/WFMD: ΔXCH4 rotat. & avg.
Norte III landfill
Buenos Aires, Argentina
Open coal mine
around Hambach, Germany
Open coal mine
around Hail Creek, Australia
Clear average plume
indicating strong isolated source
Average plume but also strong near-by sources
No average plume but local enhancement (challenging conditions)

## Slide 14: Methane: S5P/WFMD&OPER/CSF: Norte III
2021-08-18
2021-09-18
WFMD
OPER
OPER
WFMD
46 ± 19 t/h (QF=0)
37 ± 15 t/h (QF=1)
IUP-UB CSF (v1.6) algorithm applied to 2 different XCH4 data products:
Scientific WFMD v1.8
OPERational v02
OPER product used as is, i.e., without correction for striping, etc.
70 ± 36 t/h (QF=0)
95 ± 37 t/h (QF=0)

## Slide 15: Hyperspectral Imager (HI) @ 30m/60m res.
Matched Filter
PhysicsF
PCA
EnMAP
EMIT
PRISMA
Methane enhancement retrievals:
Three methods under development („HiFi“)
  Differ primarily w.r.t. forward model F & measurement error covariance matrix Sε
  PhysicsF (PF) (low order „DOAS polynomial“ e.g. for surface reflectivity, …)
  Principal Components Analysis (PCA) (PCs instead of polynomial)
  Matched Filter (MF) (e.g., no polynomial but Sε from image)
Methane emissions: CSF algorithm

## Slide 16: European localized emission sources
https://eyeclima.eu/
CSF method applied to EnMAP and EMIT

## Slide 17: European localized emission sources
https://eyeclima.eu/
CSF method applied to EnMAP and EMIT
Comparisons of landfill emission estimates:
Same EMIT scene
(§)
(§)
https://data.carbonmapper.org/
Details see talk
Bösch et al., Assessment of European localized CH4 Emission Sources with hyperspectral sensors
Today in Session A.04.01 14:00-15:30

## Slide 18: Stanford-Michigan Controlled Releases
2024 – 2025 Methane Controlled Releases
Single-blind test:
Satellite-derived emissions submitted in April 2025
„True emission“ information provided in May 2025

## Slide 19: Summary & conclusions
TROPOMI/S5P WFMD XCH4 data product:
  WFMD v1.8 product (Schneising et al., 2023) used to identify emission hotspots (Vanselow et al., 2024)
  Improved WFMD v2.0 XCH4 and XCO product available (https://www.iup.uni-bremen.de/carbon_ghg/products/tropomi_wfmd/)
Methane emission estimates via S5P and Hyperspectral Imagers:
  Cross-Sectional-Flux (CSF) algorithm
  First results from S5P, PRISMA, EnMAP, EMIT
  Emission estimates European localized sources (EYE-CLIMA)
  Detailed comparisons within MEDUSA (ongoing)
  Participation Stanford-Michigan Controlled Releases 2024/25