## Slide 1
One year of TCCON observations in Cyprus:
Data Variability and Validation/Calibration
OCO-2/OCO-3 Validation Group Meeting, 6-7 October 2020
Authors: Rousogenous C.1, Petri C.2, Warneke T.2, Quéhé P.Y.1,
Laemmel Th.3,Ramonet M.3, Notholt J.2, Vrekoussis M.1,2, Sciare J.1
1: Climate and Atmosphere Research Centre (CARE C), The Cyprus Institute (CyI)
2: Institute of Environmental Physics, Bremen, Germany
3: LSCE/IPSL, CEA-CNRS-UVSQ, Université Paris Saclay, Gif-sur-Yvette, France

## Slide 2
TCCON Nicosia: Location
In a sub-urban area
Next to a small forest
On the CyI building
35.141° N, 33.381° E, 185 m a.s.l.
Climate: Subtropical, Mediterranean, semi-arid
Population: ~ 100k
Area: ~ 110 km2
TCCON
PICARRO Inlet
Surface Measurements of CO2, CH4, CO, H2O
TCCON
PICARRO
190 m a.s.l.
185 m a.s.l.
CIMEL, AERONET/PHOTONS
PREDE, Skynet

## Slide 3
Dust
Sea Salt
Pollution
Western Europe
Pollution
Eastern Europe
+ Turkey
Dust
Pollution
Middle East
Air Masses in Cyprus: Long-range transported pollution from natural
& anthropogenic sources and seasonal variability

## Slide 4
Materialized
In progress
Auxiliary Activities
CO2 Sensor
Vertical Profiling
Airborne
Surface Mapping
In-Situ
PICARRO 1
Co-located
Surface measurements
for 1 year
Field Campaigns
PICARRO 3 Measurements In the Free Troposphere (Mt. Troodos)
PICARRO 2
Background
Measurements
ICOS Station
(West Coast)
Remote Sensing
EM27/SUN - COCCON
(to purchase)
Co-located Measurements
Field Campaigns In the MENA Region
Passive AirCore
Collaboration with LSCE
Active AirCore
on board UAS (In Progress)
SenseAir AB CO2
Integration on UAV
(Tested)
LGR ABB CO2, CH4
Integration on UAV
(In progress)
17 – 30 June 2020 Campaign
5 Flights → 3 profiles
Repeat Campaign
Summer 2021
Ceiling Altitude: 2.5Km a.g.l.
PREDE Sky Radiometer
(NIES)
Operational since:
24/07/2020
GHGs
GHGs
AOD
GHGs
GHGs

## Slide 5
1 Year of XCO2 data
High data coverage
300 – 340 sunny days per year
Up to 14 hrs of sunlight per day
Perfect location for solar absorption measurements
TCCON Nicosia:
Data Coverage and Variability
XCO2 (ppm)
Malfunction of Solar Tracker Controller

## Slide 6
CO2 (ppm)
CO (ppb)
5 x OCO-2 Validation Targets
AirCore Campaign
TCCON Nicosia: 1 Year of Data, 31/08/2019 - Now
HF (ppt)
CH4 (ppm)
N2O (ppb)
22 x OCO-3 Validation Targets
Daily means of Xgas
High variability
Tropopause altitude variations
Many validation targets

## Slide 7
1,4,5
3
2
3
1,5
4
2
  June 2020, First AirCore Campaign in Cyprus
http://predict.habhub.org
17 – 30 June
2020
@ 33 Km

## Slide 8
Asian Summer Monsoon: Transport of constituents to the tropopause level from intense convection and large scale circulation.
First AirCore Profiles for Cyprus & Comparison with CAMS Models
Distinct difference between the profile on the 19th and the ones from 29th & 30th in the upper troposphere lower stratosphere (UTLS) layer.
Action: In collaboration with LSCE and the French Aircore (AC) program, AC activities have been initiated last June in Cyprus within the framework of the EMME-CARE (Eastern Mediterranean and Middle East – Climate and Atmosphere Research).
Objective: Start a regular program of vertical profiles of greenhouse gases concentrations, combined with surface and total column observations to be integrated in ICOS and TCCON European networks.
Figures Credit: M.Ramonet

## Slide 9
TCCON Detects Asian Summer Monsoon (ASM) Long-range Pollution Transport during AirCore Campaign
Asian Summer Monsoon
AC 19/06/2020
AC 29/06/2020
AC 30/06/2020
CO2 (ppm)
CO (ppb)
CH4 (ppm)
CH4 (ppm)
CO (ppb)
CO2 (ppm)

## Slide 10: AirCore – TCCON Preliminary Comparison: XCO2 and XCH4
|Δ XCO2|: 0.2 – 0.75 ppm
up to 0.2% diff
TCCON Vs AirCore observations have good agreement
For the Xgas (aircore) calculation:
Above AirCore profile → scaled TCCON a priori
Below AirCore profile → from surface to 1st AC measurement extrapolation of bottom AC measurement up to surface pressure
|Δ XCH4|: 0 – 8 ppb
up to 0.4% diff

## Slide 11: Conclusions
TCCON Nicosia successfully installed in Cyprus and has continuous measurements for 1 year
Proximity to 3 continents and different air masses render variability in the gases.
AOD Measurements compliment remote sensing measurements
AirCore campaign successful with promising agreement with TCCON and plans for enhancing our capability for AC launches.

## Slide 12
Thank you!
Questions? 
Constantina Rousogenous
PhD Student/Graduate Research Assistant
Climate and Atmosphere Research Center (CARE-C) The Cyprus Institute 20 Konstantinou Kavafi Street, 2121, Nicosia, Cyprus Tel: +357 22208614 | Email: c.rousogenous@cyi.ac.cy Web: cyi.ac.cy | emme-care.cyi.ac.cy | cao.cyi.ac.cy
Acknowledgements
C. Keleshis1
C. Constantinides1
P. Antoniou1
J. Pernin4
C. Crevoisier4
G. Oesterman5
1: USRL, The Cyprus Institute, Nicosia, Cyprus
4: LMD/IPSL, CNRS, Ecole polytechnique, Université Paris-Saclay, Palaiseau, France
5: Jet Propulsion Laboratory, California Institute of Technology, NASA, USA